## Slide 1: TRANSISTORS
I B (PG) COLLEGE, PANIPAT
DEPARTMENTS: PHYISCS

## Slide 2: Bipolar Transistors
Two PN junctions joined together
Two types available – NPN and PNP
The regions (from top to bottom) are called the collector (C), the base (B), and the emitter (E)
Base
Collector
Emitter

## Slide 3: Operation
Begin by reverse biasing the CB junction
  Here we are showing an NPN transistor as an example
Now we apply a small forward bias on the emitter-base junction
  Electrons are pushed into the base, which then quickly flow to the collector
  The result is a large emitter-collector electron current (conventional current is C-E) which is maintained by a small E-B voltage
Some of the electrons pushed into the base by the forward bias E-B voltage end up depleting holes in that junction
  This would eventually destroy the junction if we didn’t replenish the holes
  The electrons that might do this are drawn off as a base current

## Slide 4: Currents

## Slide 5: Conventional View

## Slide 6: Origin of the names
the Emitter 'emits' the electrons which pass through the device
the Collector 'collects' them again once they've passed through the Base
...and the Base?...

## Slide 7: Original Manufacture

## Slide 8: Base Thickness
The thickness of the unmodified Base region has to be just right.
  Too thin, and the Base would essentially vanish. The Emitter and Collector would then form a continuous piece of semiconductor, so current would flow between them whatever the base potential.
  Too thick, and electrons entering the Base from the Emitter wouldn't notice the Collector as it would be too far away. So then, the current would all be between the Emitter and the Base, and there'd be no Emitter-Collector current.

## Slide 9: Amplification Properties
The C-B voltage junction operates near breakdown.
  This ensures that a small E-B voltage causes avalanche
  Large current through the device

## Slide 10: Common Base NPN

## Slide 11: Common Emitter NPN

## Slide 12: Common Collector NPN
How does IC vary with VCE for various IB?
Note that both dc sources are variable
Set VBB to establish a certain IB

## Slide 13: Collector Characteristic Curve
If VCC = 0, then IC = 0 and VCE = 0
As VCC ↑ both VCE and IC ↑
When VCE  0.7 V, base-collector becomes reverse-biased and IC reaches full value (IC = bIB)
IC ~ constant as VCE ↑. There is a slight increase of IC due to the widening of the depletion zone (BC) giving fewer holes for recombinations with e¯ in base.
Since IC = bIB, different base currents produce different IC plateaus.

## Slide 14: NPN Characteristic Curves

## Slide 15: PNP Characteristic Curves

## Slide 16: Load Line
For a constant load, stepping IB gives different currents (IC) predicted by where the load line crosses the characteristic curve. IC = bIBworks so long as the load line intersects on the plateau region of the curve.
Slope of the load line is 1/RL

## Slide 17: Saturation and Cut-off
Note that the load line intersects the 75 mA curve below the plateau region. This is saturation and IC = bIB doesn’t work in this region.
Cut-off

## Slide 18: Voltage Amplifiers
Common Base PNP
Now we have added an ac source
The biasing of the junctions are:
BE is forward biased by VBB - thus a small resistance
BC is reverse biased by VCC – and a large resistance
Since IB is small, IC  IE

## Slide 19: Equivalent ac Circuit
rE = internal ac emitter
resistance
IE = Vin/rE (Ohm’s Law)
Vout = ICRC  IERC
Recall the name – transfer resistor

## Slide 20: Current Gains
Common Base
  a = IC/IE < 1
Common Emitter
  b = IC/IB

## Slide 21: Transistors as Switches

## Slide 22: The operating points
We can control the base current using VBB (we don’t actually use a physical switch). The circuit then acts as a high speed switch.

## Slide 23: Details
In Cut-off
  All currents are zero and VCE = VCC
In Saturation
  IB big enough to produce IC(sat)  bIB
Using Kirchhoff’s Voltage Law through the ground loop
  VCC = VCE(sat) + IC(sat)RC
  but VCE(sat) is very small (few tenths), so
  IC(sat) VCC/RC

## Slide 24: Transistors with ac Input
Assume that b is such that IC varies between 20 and 40 mA. The transistor is constantly changing curves along the load line.

## Slide 25
Pt. A corresponds to the positive peak. Pt. B corresponds to the negative peak. This graph shows ideal operation.

## Slide 26: Distortion
The location of the point Q (size of the dc source on input) may cause an operating point to lie outside of the active range.
Driven to saturation
Driven into Cutoff

## Slide 27: Base Biasing
It is usually not necessary to provide two sources for biasing the transistor.
The red arrows follow the base-emitter part of the circuit, which contains the resistor RB. The voltage drop across RB is VCC – VBE (Kirchhoff’s Voltage Law). The base current is then…
and IC = bIB

## Slide 28: Base Biasing
Use Kirchhoff’s Voltage Law on the black arrowed loop of the circuit
  VCC = ICRC + VCE
  So, VCE = VCC – ICRC
  VCE = VCC – bIBRC
Disadvantge
  b occurs in the equation for both VCE and IC
  But b varies – thus so do VCE and IC
  This shifts the Q-point (b-dpendent)

## Slide 29: Transistor Amplifiers
Amplification
  The process of increasing the strength of a signal.
  The result of controlling a relatively large quantity of current (output) with a small quantity of current (input).
Amplifier
  Device use to increase the current, voltage, or power of the input signal without appreciably altering the essential quality.

## Slide 30: Class A
Entire input waveform is faithfully reproduced.
Transistor spends its entire time in the active mode
  Never reaches either cutoff or saturation.
  Drive the transistor exactly halfway between cutoff and saturation.
  Transistor is always on – always dissipating power – can be quite inefficient

## Slide 31: Class A

## Slide 32: Class B
No DC bias voltage
  The transistor spends half its time in active mode and the other half in cutoff

## Slide 33: Class AB
Between Class A (100% operation) and Class B (50% operation).

## Slide 34: Class C
IC flows for less than half then cycle. Usually get more gain in Class B and C, but more distortion

## Slide 35: Common Emitter Transistor Amplifier
Notice that VBB forward biases the emitter-base junction and dc current flows through the circuit at all times
The class of the amplifier is determined by VBB with respect to the input signal.
Signal that adds to VBB causes transistor current to increase
Signal that subtracts from VBB causes transistor current to decrease

## Slide 36: Details
At positive peak of input, VBB is adding to the input
Resistance in the transistor is reduced
Current in the circuit increases
Larger current means more voltage drop across RC (VRC = IRC)
Larger voltage drop across RC leaves less voltage to be dropped across the transistor
We take the output VCE – as input increases, VCE decreases.

## Slide 37: More details
As the input goes to the negative peak
  Transistor resistance increases
  Less current flows
  Less voltage is dropped across RC
  More voltage can be dropped across C-E
The result is a phase reversal
  Feature of the common emitter amplifier
The closer VBB is to VCC, the larger the transistor current.

## Slide 38: PNP Common Emitter Amplifier

## Slide 39: NPN Common Base Transistor Amplifier
Signal that adds to VBB causes transistor current to increase
Signal that subtracts from VBB causes transistor current to decrease
At positive peak of input, VBB is adding to the input
Resistance in the transistor is reduced
Current in the circuit increases
Larger current means more voltage drop across RC (VRC = IRC)
Collector current increases
No phase reversal

## Slide 40: PNP Common Base Amplifier

## Slide 41: NPN Common Collector Transistor Amplifier
Also called an Emitter Follower circuit – output on emitter is almost a replica of the input
Input is across the C-B junction – this is reversed biased and the impedance is high
Output is across the B-E junction – this is forward biased and the impedance is low.
Current gain is high but voltage gain is low.

## Slide 42: PNP Common Collector Transistor Amplifier

## Slide 43: Gain Factors
Usually given for common base amplifier
Usually given for common emitter amplifier
Usually given for common collector amplifier

## Slide 44: Gamma
Recall from Kirchhoff’s Current Law
  IB + IC = IE
Ex. For b = 100 a = b/(1+b) = 0.99
g = 1 + b = 101

## Slide 45: Bringing it Together
Type | Common Base | Common Emitter | Common Collector
Relation between input/output phase | 0° | 180° | 0°
Voltage Gain | High | Medium | Low
Current Gain | Low (a) | Medium (b) | High (g)
Power Gain | Low | High | Medium
Input Z | Low | Medium | High
Output Z | High | Medium | Low

## Slide 46: Various Forms
 | Common Emitter (e) | Common Base (b) | Common Collector (c)
hi (ohms) | VB/IB | VE/IB | VB/IB
hr (unitless) | VB/VC | VE/VC | VB/VE
hf (unitless) | IC/IB | IC/IE | IE/IB
ho (watts) | ICVC | ICVC | IEVE

## Slide 47
Thank You